## Slide 1
Ali Akbar Eftekhari
Exergy analysis of geothermal Energy

## Slide 2: Carnot efficiency
(Maximum) Efficiency of an ideal heat engine is only a function of:
- Heat source temperature
- Heat sink (surrounding) temperature

## Slide 3: Energy or Exergy
Heat Source @
900 K
Heat Source @
500 K
Power Cycle,
Carnot Engine
Qin
Qout,1
Qin
Power Cycle,
Carnot Engine
Qout,2
Heat Sink @ 300 K
Work
Work
Wnet = (1-300/900)Qin
= 0.67 Qin
Wnet = (1-300/500)Qin
= 0.4 Qin

## Slide 4: Heat pump
Hot zone@
Th
Heat Pump,
Reverse Carnot cycle
Qh
Qc
W
Cold zone@
Th
COP =Coefficient Of Performance

## Slide 5
1000 m
1000 m
50 m
0.25 m
3000 m
Cold Water (20oC)
Hot Water (80oC),
100 m3/hr
Exergy (W)
Power (P)

## Slide 6: Some numbers
Production rate V =100 m3 / hr = 0.028 m3 / s
Reservoir = V = 1000  1000  100 m3
Diameter well = D = 0.3 m
Heat capacity at constant pressure = Cp = 4184 J/kg/K
Downhole temperature = T2 = 80 + 273 K
Exit temperature = T0 = 40 + 273 K
Project lifetime = 20 years
Darcy velocity = u = 4.2  10-2 / 105 = 4.2  10-7 m/s
Well velocity = v = 4.2  10-3 / r2 = 0.59 m /s
Reynolds = Re = vD/ = 176838
Thermal conductivity sand : 2 W / m / K
Heat capacity sand : 2  106 J / m3 / K

## Slide 7: Pressure drop in the pipes
0.3 m
2000 m
f = friction factor:
For laminar flow
For f in other flow regimes, see Moody diagram
L = Length of pipe [m]
D = Diameter of pipe [m]
V = Liquid flow velocity [m/s]
ρ = Liquid density [kg/m3]
∆P = Pressure drop [Pa]

## Slide 8: Pressure drop in porous media
∆P = Pressure drop [Pa]
μ = Fluid viscosity [Pa.s]
k = Permeability [m2]
u = Darcy velocity [m/s]
L = Length of porous media [m]
Flow
L = 1000 m
1000 m
100 m
Flow

## Slide 9: Pumping exergy
Electrical Driver (ηd)
Power Plant (ηpp)
Fossil Fuel
Pump Mechanical Efficiency (ηp)
Exp = Pump exergy consumption [J/s]
Q = Volumetric flow of water [m3/s]
∆Ppipe = pressure drop in pipes [Pa]
∆PPM = pressure drop in porous media [Pa]

## Slide 10: Steel and Cement embodied exergy
wells | 2 |  | 
Depth | 2000 | m | 
Cement thickness | 30 | mm | 
Tube inside diameter | 300 | mm | 
Tube thickness | 10 | mm | 
0.3 m
2000 m
Steel | 58094.71 | kJ/kg
Cement | 2323.79 | kJ/kg
Steel density | 7850 | kg/m3
Cement density | 2000 | kg/m3

## Slide 11: Drilling Exergy (Rotary drilling)
Energy consumption | kJ | %
Drilling | 1.38E+008 | 1.48
Piping | 8.88E+009 | 95.33
Cementing | 2.98E+008 | 3.2
Drilling exergy consumption per meter | 68787.55 | kJ/m
Total exergy consumption | 1.38E+008 | kJ

## Slide 12: Recovery factors vs. flow rate

## Slide 13: Effect of permeability

## Slide 14: CO2 emission per unit exergy

## Slide 15: Exercise: Heating system of a room
Cold room,
Tc = 0.0oC
Qroom
Combustion of natural gas,
Th = 1800 K (AFT)
Hot water of a geothermal well,
Th = 80 + 273.15 K
Heat pump (main energy source is natural gas)
Troom= 25 +273.15 K
1
2
3
Heat Pump
Power Plant
N.G.
W
Heat
Qc
Qc
COP
η